## Slide 1
F1
F2
F3
F4
NON CONCURRENT FORCES
Lines of action are passing through multiple points.
Mechanics – 2.1
Basics of Mechanics
FY – DESH – VIT
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 2
What is Mechanics ?
It is the study of behavior of matter under the action of applied Forces.
It is a science that deals with study of Physical phenomenon.
What is Engineering Mechanics ?
It deals with …..
1) Laws and principles of Mechanics.
2) Application to the Engineering problems.
It helps an Engineer in …..
planning 2) designing 3) construction of various types of structures and machines.
e.g. Robots.
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 3
Roll of CG in Robotics
Empty Bottle
Half filled
Turned upside down !
Locate the CG of system of gripper and empty bottle
Is the CG of system at the same point ?
Where is the CG of system now ?
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 4
Facets of Engineering Mechanics : A Glance
Mechanics of Solids
Mechanics of Fluids
Mechanics of Rigid Bodies
Mechanics of Deformable Bodies
Statics
Dynamics
Kinematics
Kinetics
Elasticity
Plasticity
Ideal fluid
Viscous fluid
Incompressible fluid
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 5
Statics And Dynamics
Statics – Study of behavior of rigid bodies under the action of applied forces when they are at Rest
Dynamics – Study of behavior of rigid bodies under the action of applied forces when they are in Motion
Kinetics – Study of the Motion of the bodies due to the application of forces.
Kinematics – Study of motion of the bodies without considering the forces
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 6
Dynamics - Example
Kinematics –
How fast ??
How far ??
How long ??
Kinetics –
Which forces ?
What direction ?
Rollercoaster
Can you make a list of different physical quantities associated with this system ??
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 7
A Robot is a rigid body. (What is a Rigid Body ?)
A Robot is acted by forces at rest and in motion.
A Robot needs to have …..
    Coordination
    Synchronization
    Stability
    Balance
    within its structural parts at rest and in motion as well.
 Sound knowledge of Statics and Dynamics is necessary !
Importance of Statics and Dynamics in Robotics
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 8
Particle – Body – Rigidity – Deformation
A particle occupies a point in space with negligible dimensions and has no size and shape.
A body is composed of infinite number of particles.
A body has definite size and shape.
A body is always limited in all directions.
In a Rigid body the distance between its particles does not change under the action of the forces.
Rigid body is an idealized concept as there is no body in the Universe which is 100% Rigid.
Every body always suffers from deformation. However, if it is extremely small, can be neglected and will not change its overall dimensions.
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 9
Rigid Body
Deformable Body
Negligible
Deformation
Considerable
Distance
between particles
Negligible change
Considerable change
Equilibrium
Motion
Maintained
Disturbed
No Motion
Motion takes place
Size and
Shape
No change
Changes
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 10
What is a Force?
Force is the capacity to do work.
  Force is a vector quantity, SI unit is Newton (Kg.m/s2)
Force produces motion in the body.
  Force causes…. 1) Translation or 2) Rotation or 3) both.
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 11
A Force has ………
Magnitude – for e.g. 100 Newtons.
Direction – angle made with + X axis. For e.g….
1 = + 500 i.e. CCW (1st Quadrant)
2 = – 400 i.e. CW (4th Quadrant)
Sense – either a Push or a Pull.
Point of Application of Force – It is the point on the body at which the force can be assumed to be concentrated.
Line of Action of Force – The line in which the force tends to move the body.
F
F
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 12
Force System
A “Force System” consists of multiple forces acting on a body at a point.
Types of Force system are …..
1) Co-planar and Non-Coplanar Force system
2) Concurrent and Non-Concurrent Force system
3) Parallel and Non-Parallel Force system
4) Collinear and Non-Collinear Force system
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 13
Co-Planar and Non Co-Planar Force system
Non Co-Planer Forces
Co-Planer Forces
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 14
Concurrent and Non-concurrent force system
Lines of action are passing through a common point.
CONCURRENT FORCES
NON CONCURRENT FORCES
Lines of action are passing through multiple points.
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 15
Parallel , Anti Parallel and Non-Parallel Forces
PARALLEL FORCES
ANTI - PARALLEL FORCES
F1
F2
F3
F4
NON-PARALLEL FORCES
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 16
Collinear and Non Collinear force system
CO-LINEAR FORCE SYSTEM
F1
F2
F3
F4
WHAT IS THIS SYSTEM ?
IS IT NON-CONCURRENT ?
IS IT CO-PLANER ?
SAFETY FALL NET
IS IT PARALLEL ?
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 17
Principle of Transmissibility of Force -
“If a force acts at a point on a rigid body, then it is assumed to act at any point on the line of action of force within the body.”
P
C
B
A
Line of action of the Force
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 18
Resolution of a Force -
Along….. 1) X axis 2) Y axis
Force is a vector quantity. So, it can be assumed to be composed of two fictitious components.
X
Y
Force F

F cos 
F sin 
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 19
Resultant Force -
F1
F2
F3
F4
Resultant Force
F1
F2
F3
F4
Resultant Force = vector sum of all forces.
(algebraic sum)
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 20
Law of Parallelogram of Forces -
X
Y
R = Resultant is the diagonal

P
Q
P and Q are coplaner and concurrent forces
Is Pythagoras theorem related to this ?
R = P2 + Q2 + 2 P Q cos
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 21
Law Of Parallelogram of Forces - Derivation
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 22
Law Of Parallelogram of Forces -
CD CD Q sin 
tan  = -------- = -------------- = ------------------
OD OA + AD P + Q cos 
Q sin 
 = tan-1 ( --------------------)
P + Q cos 
IMP Note -  is the angle of the Resultant w.r.t. Force P .
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 24
Equilibrium -
A rigid body is said to be in equilibrium, when the resultant of the force system on it is zero.
The resultant of the force system can be a Force or a Moment.
If the resultant is zero, it implies that the resultant force (∑ F) and resultant moment (∑ M) both are zero.
If the resultant force ∑ F = 0, there is No Translation.
Thus the body is said to be in a …….Complete Static Equilibrium
If the resultant moment ∑ M = 0, there is No Rotation.
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 25
Equilibrant = the balancing Force which brings m
Equilibrant is a force which is …..
1) equal in magnitude
2) opposite in direction
3) collinear to the resultant of the force system.
Equilibrium is achieved when, all are satisfied.
1) ∑ Fx = 0 ….. X components
2) ∑ Fy = 0 ….. Y components
3) ∑ M = 0 ….. Moments
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 26
Free Body Diagram (F.B.D.) - (Short sketch of the system)
In a physical system, to study the equilibrium, the actual machine parts and structures are replaced by respective active, passive forces, reactions and moments.
FBD features ….
It is a sketch of a body of interest only.
All the surrounding bodies are removed.
All of the forces acting on the body are considered and shown.
All of the forces acted by the body on other bodies are NOT considered.
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 27
How to draw Free Body Diagram ? -
A sphere of weight W is resting on a rigid wall and is held by a string as shown……
Draw the FBD of the sphere.
W
W
R
T
T
R
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 28
Lami's Theorem -
If there are a few forces acting on a body and the body is in a static equilibrium, then according to Lami’s Theorem ……….
P Q R
-------- = --------- = ---------
sin a sin b sin c
P
Q
R
a
b
c
P, Q and R are the 3 forces keeping the body in equilibrium.
a, b and c are the respective angles.
Also called as law of sines.
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 29
Numerical Example 1 -
Find the resultant Force R if …..
F1 = 40 N, F2 = 80 N, F3 = 60 N and F4 = 30 N
and the respective angles are ……
1 = 450, 2 = 1500, 3 = 2400, 4 = - 400
F1 = 40 N
F2 = 80 N
F3 = 60 N
F4 = 30 N
-400
2400
1500
450
IMP Note - All angles are measured from +ve X axis.
CCW angles are +ve
CW angles are –ve
Thus, + 600 = - 3000
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 30
Ex. 1 Solution -
Resolve each Force into X and Y components and sum up.
F1 = 40 N
F2 = 80 N
F3 = 60 N
F4 = 30 N
-400
2400
1500
450
Note : F1 = 40 N450 is the polar format. Convert it to Rectangular (Cartesian) using P to R function on calculator. Pol (+) and Rec (-)
F1 = 40 N 450 = ( 28.2842, 28.2842 )
F2 = 80 N 1500 = ( -69.2820, 40 )
F3 = 60 N 2400 = ( -30, -51.9615 )
F4 = 30 N - 400 = ( 21.2132, -21.2132 )
 Fx = - 49.7846 ,  Fy = - 4.8905
Convert to Polar
 R = 50.0242 N  -174.390 … Answer
IMP : All angles are measured from +ve X axis.
CW = – ve and CCW = + ve
R = 50.0242 N
 =  -174.390
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 31
Numerical Example 2 -
Find the magnitudes of components of the force F of 750 N in the directions OP and OQ.
F = 750 N
200
150
X
Y
P
Q
200
O
Can you find this angle ?
650
?
What is angle  POQ = ?
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 32
Ex. 2 - Solution
F = 750 N
200
150
X
Y
P
Q
200
O
Formulae –
F along P = F * [ sin FQ / sin (FP + FQ) ]
F along Q = F * [ sin FP / sin (FP + FQ) ]
FP = F * [ sin FQ / sin (FP + FQ) ]
= 750 * [ sin 65 / sin (65 + 20) ]
= 682.3273 N
FQ = F * [ sin FP / sin (FP + FQ) ]
= 750 * [ sin 20 / sin (65 + 20) ]
= 257.4949 N ….. Answer
This is just opposite to the Parallelogram Law.
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 33
F1
F2
F3
F4
NON CONCURRENT FORCES
Lines of action are passing through multiple points.
Mechanics – 2.1
Basics of Mechanics
Thanks !
FY – DESH – VIT
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities