## Slide 1
N
S
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities
Actuators – 3.2
Basics of Magnetism
FY – DESH – VIT

## Slide 2
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities
The Earth – Magnetism - Poles
Where is Magnetic North Pole of Earth ?
Why the Earth shows Magnetic properties ?
Is Geographical axis same as Magnetic axis ?
Where is the Magnetic axis ?
Are both axes matching ?
Try these questions –
Just as a curiosity !
What is the exact location of Magnetic Poles of Earth ?

## Slide 3
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities
Earth as a huge Magnet .....
The Earth is a huge Magnet with its
Magnetic North pole at its Geographical South pole
and vice versa .....

## Slide 4
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities
The number of unpaired electrons and their CW or CCW spins are mainly responsible for the Magnetism along with the crystal structure.
Electron Spin
Electronic Configuration of Iron
The origin of Magnetism

## Slide 5
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities
Properties of Magnetic Lines of Force -
1) Magnetic lines are invisible, imaginary lines which are somewhat elliptical in shape which never cross eachother.
3) Magnetic lines that are parallel and travelling in the same direction, REPEL eachother.
4) Magnetic lines act like stretched rubber band which always try to contract.
5) Magnetic lines prefer a path of minimum reluctance.
2) Magnetic lines are closed loops that are supposed to travel from North pole of a bar magnet towards the South pole external to the magnet and from South pole towards the North pole internally.

## Slide 6
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities
S
N
S
N
S
N
Concept of Orientation of Magnetic Flux in a material -
S
N

## Slide 7
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities
Match the pairs
A
B
1) Left hand rule
2) Right hand thumb rule
3) Right hand rule
A) Generating action
B) Motoring action
C) Direction of magnetic field due of current
4) Right hand grip rule
D) Magnetic attraction
5) Left hand screw rule
E) Lenz’s Law
F) Faraday’s 2nd Law
6) Fleming’s Left hand rule
7) Fleming’s Right hand rule
G) Faraday’s 1st Law

## Slide 8
Will the two conductors attract or repel ?
…. And what about this …?
Cross conductor
Dot conductor
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 9
The conductors will get repelled
The conductors will get attracted
Lines that are travelling in the same direction REPEL eachother
Lines that are travelling in the opposite direction ATTRACT eachother
Attraction or Repulsion is a property of the direction of magnetic lines
Cross conductor
Dot conductor
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 10
Right Hand Thumb Rule
Which one of the above is correct ??
Thumb is for Current or Field ??
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 11
Important terms related to Magnetism -
Magnetic Permeability (  ) : It is the property of a material to allow the magnetic line of force to pass through it.
Unit is Henry per meter ( H / meter)
Relative Permeability : It is just a ratio for comparison
         of the material
         r = --------------------------- ( No unit)
         of air or vacuum
        A good ferromagnetic material is about 800 to 1200 times better than air.
Value of r for air = ??
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 12
Important terms related to Magnetism -
Magnetic Field Strength OR
Magnetic Field Intensity OR
Magnetising Force ( H ) : MMF reqd. per meter length
Unit is Ampere-Turns per meter ( Amp / meter)
Magneto Motive Force MMF ( F ) : (Similar to EMF)
F = No. of Turns x Current through them
F = N x I Unit = Amp-Turns (OR Amp)
Magnetic Flux Density ( B ) :
Flux Weber
B = ------- Unit is Tesla ( T ) = ---------------
Area Sq. meter
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 13
Important terms related to Magnetism -
MMF (F) Amp x Turns
Flux () = -------------------- = -----------------------
Reluctance (s) (1 / ) x ( l / a)
I N
Flux () = --------------------
(1 / ) x ( l / a)
We know that, H = B / 
 I N a I N
Substituting for B and  , H = --- x --------- = --------
a  l l
 l
From above we get ,  = ----------
I N a
Thus, H is a function of the Current I which produces the Flux  ........ H  I
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 14
Magnetising
Force H
Flux density B
B-H Curve Hysteresis Loop
O
A
B
C
D
E
F
G
H
Sluggish start
Linear rise
Saturation
OD = Retaintivity
(Residual Magnetism)
Magnetism lost
Saturation
OG = Retaintivity
(Residual Magnetism)
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 15
Magnetising
Force H
Flux density B
B-H Curve
Hysteresis Loop
O
A
B
C
D
E
F
G
H
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 16
1
2
3
4
5
Comment on all the curves -
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 17
1) Draw graph of IDEAL magnetic material
2) Is a good conductor, magnetic in nature ?
3) Is a good magnetic material, a conductor ?
4) What is Curie temperature ?
5) Write on similarities and differences between Electrical and Magnetic circuits
Home work –
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities

## Slide 18
N
S
Vishwakarma Institute of Technology
FY - Department of Engineering, Sciences and Humanities
Actuators – 3.2
Thanks !
Basics of Magnetism
FY – DESH – VIT